## Slide 1: CS314 Computer Organization Fall 2017 Chapter 2: Instructions: Language of the Computer
Haojin Zhu (http://tdt.sjtu.edu.cn/~hjzhu/ )
Course Website: http://nsec.sjtu.edu.cn/teaching/ei209.html
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2012, MK]
Notes: Combinations to AV system, etc. 0808 (1988 in 113 IST)
Call AV hot line at 8-777-0035

## Slide 2: MIPS Instruction Fields
MIPS fields are given names to make them easier to refer to
op rs rt rd shamt funct
op 6-bits opcode that specifies the operation
rs 5-bits register file address of the first source operand
rt 5-bits register file address of the second source operand
rd 5-bits register file address of the result’s destination
shamt 5-bits shift amount (for shift instructions)
funct 6-bits function code augmenting the opcode

## Slide 3: MIPS Memory Access Instructions
MIPS has two basic data transfer instructions for accessing memory
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data is loaded into (lw) or stored from (sw) a register in the register file – a 5 bit address
The memory address – a 32 bit address – is formed by adding the contents of the base address register to the offset value
  A 16-bit field meaning access is limited to memory locations within a region of 213 or 8,192 words (215 or 32,768 bytes) of the address in the base register
Notes: Note that the offset can be positive or negative.
Offsets must be able to access bytes as well, so word offsets will have two low-order zeros in them.

## Slide 4: Machine Language - Load Instruction
Load/Store Instruction Format (I format):
lw $t0, 24($s3)
35 19 8 2410
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s3
0x12004094
2410 + $s3 =
. . . 0001 1000
+ . . . 1001 0100
. . . 1010 1100 =
0x120040ac
0x120040ac
$t0
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 5: Byte Addresses
Since 8-bit bytes are so useful, most architectures address individual bytes in memory
  Alignment restriction - the memory address of a word must be on natural word boundaries (a multiple of 4 in MIPS-32)
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Notes: Talk about the reasons (performance) for the word/byte alignment restriction

## Slide 6: Aside: Loading and Storing Bytes
MIPS provides special instructions to move bytes
lb $t0, 1($s3) #load byte from memory
sb $t0, 6($s3) #store byte to memory
0x28 19 8 16 bit offset
What 8 bits get loaded and stored?
  load byte places the byte from memory in the rightmost 8 bits of the destination register
    what happens to the other bits in the register?
  store byte takes the byte from the rightmost 8 bits of a register and writes it to a byte in memory
    what happens to the other bits in the memory word?
Notes: load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register
Store byte leaves the other bits in the memory word intact.

## Slide 7: Example of Loading and Storing Bytes
Given following code sequence and memory state what is the state of the memory after executing the code?
add $s3, $zero, $zero
lb $t0, 1($s3)
sb $t0, 6($s3)
Memory
0x 0 0 9 0 1 2 A 0
Data
Word
Address (Decimal)
0
4
8
12
16
20
24
0x F F F F F F F F
0x 0 1 0 0 0 4 0 2
0x 1 0 0 0 0 0 1 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
What value is left in $t0?
What if the machine was little Endian?
What word is changed in Memory and to what?
Notes: For class handout

## Slide 8: Example of Loading and Storing Bytes
Given following code sequence and memory state what is the state of the memory after executing the code?
add $s3, $zero, $zero
lb $t0, 1($s3)
sb $t0, 6($s3)
Memory
0x 0 0 9 0 1 2 A 0
Data
Word
Address (Decimal)
0
4
8
12
16
20
24
0x F F F F F F F F
0x 0 1 0 0 0 4 0 2
0x 1 0 0 0 0 0 1 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
0x 0 0 0 0 0 0 0 0
$t0 = 0x00000090
mem(4) = 0xFFFF90FF
mem(4) = 0xFF12FFFF
What value is left in $t0?
What if the machine was little Endian?
What word is changed in Memory and to what?
$t0 = 0x00000012
Notes: For lecture
Big Endian Little Endian
0 1 2 3 3 2 1 0
$t0 gets 90 $t0 gets 12
word 4 gets FFFF90FF word 4 gets FF12FFFF

## Slide 9: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 Bytes)
  Memory: Billions of bytes (2 GB to 8 GB on laptop)
and the RISC principle is…
  Smaller is faster
How much faster are registers than memory??
About 100-500 times faster!
  in terms of latency of one access

## Slide 10: MIPS Immediate Instructions
addi $sp, $sp, 4 #$sp = $sp + 4
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
Machine format (I format):
0x0A 18 8 0x0F
Small constants are used often in typical code
Possible approaches?
  put “typical constants” in memory and load them
  create hard-wired registers (like $zero) for constants like 1
  have special instructions that contain constants !
The constant is kept inside the instruction itself!
  Immediate format limits values to the range +215–1 to -215
what about upper 16 bits?
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers
much faster than if loaded from memory
addi and slti do sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 11: Aside: How About Larger Constants?
We'd also like to be able to load a 32 bit constant into a register, for this we must use two instructions
a new "load upper immediate" instruction
lui $t0, 1010101010101010
Then must get the lower order bits right, use ori $t0, $t0, 1010101010101010
16 0 8 10101010101010102
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
why can’t addi be used as the second instruction for this 32 bit constant?
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically

## Slide 12: Review: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 13: Possible Representations of Computers
Sign Mag. | Two’s Comp. | One’s Comp.
 | 1000 = -8 | 
1111 = -7 | 1001= -7 | 1000 = -7
1110 = -6 | 1010 = -6 | 1001 = -6
1101 = -5 | 1011 = -5 | 1010 = -5
1100 = -4 | 1100 = -4 | 1011 = -4
1011 = -3 | 1101 = -3 | 1100 = -3
1010 = -2 | 1110 = -2 | 1101 = -2
1001 = -1 | 1111 = -1 | 1110 = -1
1000 = -0 |  | 1111 = -0
0000 = +0 | 0000 = 0 | 0000 = +0
0001 = +1 | 0001 = +1 | 0001 = +1
0010 = +2 | 0010 = +2 | 0010 = +2
0011 = +3 | 0011 = +3 | 0011 = +3
0100 = +4 | 0100 = +4 | 0100 = +4
0101 = +5 | 0101 = +5 | 0101 = +5
0110 = +6 | 0110 = +6 | 0110 = +6
0111 = +7 | 0111 = +7 | 0111 = +7
Which one is best? Why?

## Slide 14: Review: Signed Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
complement all the bits
0101
and add a 1
0110
why it holds?
Notes: Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)

## Slide 15: MIPS Shift Operations
Need operations to pack and unpack 8-bit characters into 32-bit words
Shifts move all the bits in a word left or right
sll $t2, $s0, 8 #$t2 = $s0 << 8 bits
srl $t2, $s0, 8 #$t2 = $s0 >> 8 bits
Instruction Format (R format)
Such shifts are called logical because they fill with zeros
  Notice that a 5-bit shamt field is enough to shift a 32-bit value 25 – 1 or 31 bit positions
0 16 10 8 0x00
Notes: also have sllv, srlv, and srav

## Slide 16: MIPS Logical Operations
There are a number of bit-wise logical operations in the MIPS ISA
and $t0, $t1, $t2 #$t0 = $t1 & $t2
or $t0, $t1, $t2 #$t0 = $t1 | $t2
nor $t0, $t1, $t2 #$t0 = not($t1 | $t2)
Instruction Format (R format)
andi $t0, $t1, 0xFF00 #$t0 = $t1 & ff00
ori $t0, $t1, 0xFF00 #$t0 = $t1 | ff00
Instruction Format (I format)
0 9 10 8 0 0x24
0x0D 9 8 0xFF00

## Slide 17: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
0x05 16 17 16 bit offset
How is the branch destination address specified?

## Slide 18: Specifying Branch Destinations
Use a register (like in lw and sw) added to the 16-bit offset
  which register? Instruction Address Register (the PC)
    its use is automatically implied by instruction
    PC gets updated (PC+4) during the fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 (word) instructions from the (instruction after the) branch instruction, but most branches are local anyway
PC
Add
32
32
32
32
32
offset
16
32
00
sign-extend
from the low order 16 bits of the branch instruction
branch dst
address
?
Add
4
32
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 19: In Support of Branch Instructions
We have beq, bne, but what about other kinds of branches (e.g., branch-if-less-than)? For this, we need yet another instruction, slt
Set on less than instruction:
slt $t0, $s0, $s1 # if $s0 < $s1 then # $t0 = 1 else # $t0 = 0
Instruction format (R format):
Alternate versions of slt
slti $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
sltu $t0, $s0, $s1 # if $s0 < $s1 then $t0=1 ...
sltiu $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
2
0 16 17 8 0x24
Notes: Unsigned (u) versus signed integer comparison

## Slide 20: Aside: More Branch Instructions
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
slt $at, $s1, $s2 #$at set to 1 if
bne $at, $zero, Label #$s1 < $s2
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
Notes: For lecture
blt $s1,$s2 Label =
slt $at,$s1,$s2 #at gets 1 if $s1 < $s2
bne $at,$zero,Label

## Slide 21
MIPS Instructions
Consider a comparison instruction:
slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?

## Slide 22
MIPS Instructions
Consider a comparison instruction:
slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?
The result depends on whether $t1 is a signed or unsigned
number – the compiler/programmer must track this and
accordingly use either slt or sltu
slt $t0, $t1, $zero stores 1 in $t0
sltu $t0, $t1, $zero stores 0 in $t0

## Slide 23: Bounds Check Shortcut
Treating signed numbers as if they were unsigned gives a low cost way of checking if 0 ≤ x < y (index out of bounds for arrays)
sltu $t0, $s1, $t2 # $t0 = 0 if # $s1 > $t2 (max) # or $s1 < 0 (min) beq $t0, $zero, IOOB # go to IOOB if # $t0 = 0
The key is that negative integers in two’s complement look like large numbers in unsigned notation. Thus, an unsigned comparison of x < y also checks if x is negative as well as if x is less than y.

## Slide 24: Other Control Flow Instructions
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Instruction Format (J Format):
0x02 26-bit address
PC
4
32
26
32
00
from the low order 26 bits of the jump instruction
Why shift left by two bits?
Notes: If-then-else code compilation

## Slide 25: Aside: Branching Far Away
What if the branch destination is further away than can be captured in 16 bits?
The assembler comes to the rescue – it inserts an unconditional jump to the branch target and inverts the condition
beq $s0, $s1, L1
becomes
bne $s0, $s1, L2
j L1
L2:

## Slide 26: Compiling Another While Loop
Compile the assembly code for the C while loop where i is in $s3, k is in $s5, and the base address of the array save is in $s6
while (save[i] == k) i += 1;
Notes: For class handout

## Slide 27: Compiling Another While Loop
Compile the assembly code for the C while loop where i is in $s3, k is in $s5, and the base address of the array save is in $s6
while (save[i] == k) i += 1;
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: . . .
Notes: For lecture

## Slide 28
Can make a “for” loop with only j
Can make a “for” loop with only beq
Code for “else” part can come before code for “then” in translation of “if”
Can make an unconditional branch from a
conditional branch instruction
☐
☐
☐
☐
Which of the following is FALSE?

## Slide 29: Review: MIPS Addressing Modes Illustrated
1. Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand
3. Immediate addressing
op rs rt operand
4. PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 30: End of Lecture #1
The next topic is procedure

## Slide 31: Instructions for Accessing Procedures
MIPS procedure call instruction: jal ProcedureAddress #jump and link
Saves PC+4 in register $ra to have a link to the next instruction for the procedure return
Machine format (J format):
Then can do procedure return with a
jr $ra #return
Instruction format (R format):
0x03 26 bit address
0 31 0x08
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 32: Six Steps in Execution of a Procedure
Main routine (caller) places parameters in a place where the procedure (callee) can access them
  $a0 - $a3: four argument registers
Caller transfers control to the callee
Callee acquires the storage resources needed
Callee performs the desired task
Callee places the result value in a place where the caller can access it
  $v0 - $v1: two value registers for result values
Callee returns control to the caller
  $ra: one return address register to return to the point of origin

## Slide 33: MIPS Function Call Conventions
Registers faster than memory, so use them
$a0–$a3: four argument registers to pass parameters
$v0–$v1: two value registers to return values
$ra: one return address register to return to the point of origin
(7 + $zero +$at of 32, 23 left!)
$t0-$t9: 10 x temporaries (intermediates)
$s0-$s7: 8 x “saved” temporaries (program variables)
18 registers
32 – (18 + 9) = 5 left
Notes: $at – assembler temporary register, used for pseudo instructions

## Slide 34: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? ????
Student Roulette?

## Slide 35: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke X (callee)
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter, it doesn’t count programs!
jr $ra puts address inside $ra into PC
What value does jal X place into $ra? Next PC
PC + 4

## Slide 36: Aside: Spilling Registers
What if the callee needs to use more registers than allocated to argument and return values?
  callee uses a stack – a last-in-first-out queue
low addr
high addr
$sp
One of the general registers, $sp ($29), is used to address the stack (which “grows” from high address to low address)
  add data onto the stack – push
    $sp = $sp – 4 data on stack at new $sp
  remove data from the stack – pop
    data from stack at $sp $sp = $sp + 4
top of stack
(28 out of 32, 4 left!)
Notes: Note that temporary registers $t0 through $t9 can also be used as by MIPS convention they are not preserved by the callee (kept intact) across subroutine boundaries
However, saved registers $s0 through $s7 must be preserved by the calle - I.e., if the callee uses one, it must first save it and then restore it to its old value before returning control to the caller

## Slide 37: Compiling a C Leaf Procedure
Leaf procedures are ones that do not call other procedures. Give the MIPS assembler code for
int leaf_ex (int g, int h, int i, int j)
{ int f;
f = (g+h) – (i+j);
return f; }
where g, h, i, and j are in $a0, $a1, $a2, $a3
Notes: For class handout

## Slide 38: Compiling a C Leaf Procedure
Leaf procedures are ones that do not call other procedures. Give the MIPS assembler code for
int leaf_ex (int g, int h, int i, int j)
{ int f;
f = (g+h) – (i+j);
return f; }
where g, h, i, and j are in $a0, $a1, $a2, $a3
Notes: For lecture
When using temporary registers, must assume their old values must be saved and restored.
Show the stack contents on the board as you progress through the code

## Slide 39: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j are passed in $a0, …, $a3
  f in $s0 (we need to save $s0 on stack – we will see why later)
  Results are returned in $v0, $v1
$a0
$a1
$a2
$a3
$v0
$v1
argument registers
result registers
procedure

## Slide 40: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements
Example:

## Slide 41: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Restore $s0
Result
Return

## Slide 42: Procedure Call Mechanics
Old Stack Frame
arg registers
return address
Saved registers
local variables
New Stack
Frame
$fp
$fp
$sp
$sp
Low Address
High Address
compiler
ISA
HW
compiler
addressing
$gp
PC
$sp
stack
dynamic data
static data
text
reserved
System Wide Memory Map

## Slide 43: Nested Procedures
What happens to return addresses with nested procedures?
int rt_1 (int i) {
if (i == 0) return 0;
else return rt_2(i-1); }
caller: jal rt_1 next: . . .
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $a0, $a0, -1
jal rt_2
jr $ra
rt_2: . . .
Notes: So caller must save $ra on the stack and callee must save any other registers that it uses on the stack

## Slide 44: Nested Procedures Outcome
caller: jal rt_1 next: . . .
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $a0, $a0, -1
jal rt_2
jr $ra
rt_2: . . .
On the call to rt_1, the return address (next in the caller routine) gets stored in $ra. What happens to the value in $ra (when i != 0) when rt_1 makes a call to rt_2?
Notes: So caller must save $ra on the stack and callee must save any other registers that it uses on the stack

## Slide 45: Saving the Return Address, Part 1
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
low addr
high addr
$sp
$ra
old TOS
Notes: For class handout

## Slide 46: Saving the Return Address, Part 1
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
caller rt addr
high addr
 $sp
$sp
low addr
old $a0
$ra
caller rt addr
bk_2
old TOS
Notes: For lecture
Note that the original values of $ra and I ($a0) are restored on return
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 47: Saving the Return Address, Part 2
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
low addr
high addr
$sp
$ra
old TOS
Notes: For class handout

## Slide 48: Saving the Return Address, Part 2
Nested procedures (i passed in $a0, return value in $v0)
rt_1: bne $a0, $zero, to_2
add $v0, $zero, $zero
jr $ra
to_2: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $a0, -1
jal rt_2
bk_2: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra
Save the return address (and arguments) on the stack
caller rt addr
high addr
$sp
 $sp
low addr
old $a0
$ra
bk_2
caller rt addr
old TOS
Notes: For lecture

## Slide 49: MIPS Register Convention
Name | Register Number | Usage | Preserve on call?
$zero | 0 | the constant 0 | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes
Notes: $a0-$a3 – used to pass parameters, loaded by caller, read by callee and preserved by callee
$v0-$v1 – used to pass results back from callee to caller (note, can also use to pass parameters from caller to callee by is NOT preserved)

## Slide 50: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame
(29 of 32, 3 left!)

## Slide 51: Stack Before, During, After Call

## Slide 52: Compiling a Recursive Procedure
A procedure for calculating factorial
int fact (int n) {
if (n < 1) return 1;
else return (n * fact (n-1)); }
A recursive procedure (one that calls itself!)
  fact (0) = 1
  fact (1) = 1 * 1 = 1
  fact (2) = 2 * 1 * 1 = 2
  fact (3) = 3 * 2 * 1 * 1 = 6
  fact (4) = 4 * 3 * 2 * 1 * 1 = 24
  . . .
Assume n is passed in $a0; result returned in $v0

## Slide 53: Compiling a Recursive Procedure
fact: addi $sp, $sp, -8 #adjust stack pointer
sw $ra, 4($sp) #save return address
sw $a0, 0($sp) #save argument n
slti $t0, $a0, 1 #test for n < 1
beq $t0, $zero, L1 #if n >=1, go to L1
addi $v0, $zero, 1 #else return 1 in $v0
addi $sp, $sp, 8 #adjust stack pointer
jr $ra #return to caller (1st)
L1: addi $a0, $a0, -1 #n >=1, so decrement n
jal fact #call fact with (n-1)
#this is where fact returns
bk_f: lw $a0, 0($sp) #restore argument n
lw $ra, 4($sp) #restore return address
addi $sp, $sp, 8 #adjust stack pointer
mul $v0, $a0, $v0 #$v0 = n * fact(n-1)
jr $ra #return to caller (2nd)
Using stacks to save existing data in $ra and $a0
Make the branch
Call procedure
Fact(n-1)
Return Fact(1)
Return after procedure
Fact(n-1)
Notes: Note, no need to load $ra, and $a0, since they have not changed values (expect when n is >= to 1 as on next page)
We assume a multiply instruction is available, even though we haven’t covered it yet!

## Slide 54: A Look at the Stack for $a0 = 2, Part 1
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with jal (second call to fact routine with $a0 now holding 1)
  saved return address to caller routine (i.e., location in the main routine where first call to fact is made) on the stack
  saved original value of $a0 on the stack
Notes: For class handout

## Slide 55: A Look at the Stack for $a0 = 2, Part 1
 $sp
$ra
$a0
$v0
$sp
caller rt addr
caller rt addr
$a0 = 2
2
1
bk_f
old TOS
Stack state after execution of the first encounter with jal (second call to fact routine with $a0 now holding 1)
  saved return address to caller routine (i.e., location in the main routine where first call to fact is made) on the stack
  saved original value of $a0 on the stack
Notes: For lecture
NEXT TIME - Add tracking of the PC to the animation!!

## Slide 56: A Look at the Stack for $a0 = 2, Part 2
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the second encounter with jal (third call to fact routine with $a0 now holding 0)
  save return address of instruction in caller routine (instruction after jal) on the stack
  save previous value of $a0 on the stack
Notes: For class handout

## Slide 57: A Look at the Stack for $a0 = 2, Part 2
$ra
$a0
$v0
 $sp
caller rt addr
$a0 = 2
1
0
bk_f
old TOS
$sp
$a0 = 1
bk_f
bk_f
Stack state after execution of the second encounter with jal (third call to fact routine with $a0 now holding 0)
  saved return address of instruction in caller routine (instruction after jal) on the stack
  saved previous value of $a0 on the stack
Notes: For lecture

## Slide 58: A Look at the Stack for $a0 = 2, Part 3
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with the first jr ($v0 initialized to 1)
  stack pointer updated to point to third call to fact
Notes: For class handout

## Slide 59: A Look at the Stack for $a0 = 2, Part 3
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
0
old TOS
 $sp
$a0 = 0
bk_f
bk_f
$a0 = 2
caller rt addr
1
$sp
Stack state after execution of the first encounter with the first jr ($v0 initialized to 1)
  stack pointer updated to point to third call to fact
Notes: For lecture

## Slide 60: A Look at the Stack for $a0 = 2, Part 4
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the first encounter with the second jr (return from fact routine after updating $v0 to 1 * 1)
  return address to caller routine (bk_f in fact routine) restored to $ra from the stack
  previous value of $a0 restored from the stack
  stack pointer updated to point to second call to fact
Notes: For class handout

## Slide 61: A Look at the Stack for $a0 = 2, Part 4
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
0
old TOS
$a0 = 0
bk_f
$a0 = 2
caller rt addr
1
$sp
1
bk_f
1 * 1
Stack state after execution of the first encounter with the second jr (return from fact routine after updating $v0 to 1 * 1)
  return address to caller routine (bk_f in fact routine) restored to $ra from the stack
  previous value of $a0 restored from the stack
  stack pointer updated to point to second call to fact
Notes: For lecture

## Slide 62: A Look at the Stack for $a0 = 2, Part 5
$sp
$ra
$a0
$v0
old TOS
Stack state after execution of the second encounter with the second jr (return from fact routine after updating $v0 to 2 * 1 * 1)
  return address to caller routine (main routine) restored to $ra from the stack
  original value of $a0 restored from the stack
  stack pointer updated to point to first call to fact
Notes: For class handout

## Slide 63: A Look at the Stack for $a0 = 2, Part 5
$ra
$a0
$v0
 $sp
bk_f
$a0 = 1
1
old TOS
$a0 = 0
bk_f
$a0 = 2
caller rt addr
1 * 1
$sp
2
bk_f
2 * 1 * 1
Stack state after execution of the second encounter with the second jr (return from fact routine after updating $v0 to 2 * 1 * 1)
  return address to caller routine (main routine) restored to $ra from the stack
  original value of $a0 restored from the stack
  stack pointer updated to point to first call to fact
caller rt addr
Notes: For lecture

## Slide 64: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 65: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
  (30 of 32, 2 left! – will see when talk about OS)
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 66: MIPS Memory Allocation

## Slide 67
jal saves PC+1 in %ra
The callee can use temporary registers (%ti) without saving and restoring them
The caller can rely on save registers (%si) without fear of callee changing them
MIPS uses jal to invoke a function and jr to return from a function
☐
☐
☐
☐
Which statement is FALSE?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 68: Assignment II
Chapter II: 2.4, 2.14, 2.20
Submission Deadline: Oct 26