## Slide 1: Solutions Chapter 2

## Slide 2: Exercise 2.4
The following problems deal with translating from C to MIPS. Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively. Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively.
a. f = -g - A[4];
b. B[8] = A[i - j]

## Slide 3
2.4.1 For the C statement above, what is the corresponding MIPS assembly code?
Solution:
a. lw $s0, 16($s6)
sub $s0, $0, $s0
sub $s0, $s0, $s1
b. sub $t0, $s3, $s4
slli $t0, $t0, 2
add $t0, $s6, $t0
lw $t1, 0($t0)
sw $t1, 32($s7)

## Slide 4
2.4.2 For the C statements above, how many MIPS assembly instructions are needed to perform the C statement?
Solution:
a. 3
b. 5

## Slide 5
2.4.3 For the C statement above, how many different registers are needed to carry out the C statement?
Solution:
a. 3
b. 6

## Slide 6
The following problems deal with translating from MIPS to C. Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively. Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively.
a. slli $s2, $s4, 1 // h=j*2
add $s0, $s2, $s3 // f=j*2+i
add $s0, $s0, $s1 // f=j*2+i+g
b. add $t0, $s6, $s0 //t0= &A[f/4]
add $t1, $s7, $s1 // t1= &B[g/4]
lw $s0, 0($t0) //s0= A[f/4]
addi $t2, $t0, 4 //t2= &A[f/4+1]
lw $t0, 0($t2) // t0= A[f/4+1]
add $t0, $t0, $s0 // t0= A[f/4]+ A[f/4+1]
sw $t0, 0($t1) // B[g/4]= A[f/4]+ A[f/4+1]

## Slide 7
2.4.4 For the MIPS assembly instructions above, what is the corresponding C statement?
Solution:
a. f = 2j + i + g;
b. B[g] = A[f] + A[1+f];

## Slide 8
2.4.5 For the MIPS assembly instructions above, rewrite the assembly code to minimize the number if MIPS instructions (if possible) needed to carry out the same function.
Solution:
a. slli $s2, $s4, 1
add $s0, $s2, $s3
add $s0, $s0, $s1
b. add $t0, $s6, $s0
add $t1, $s7, $s1
lw $s0, 0($t0)
lw $t0, 4($t0)
add $t0, $t0, $s0
sw $t0, 0($t1)

## Slide 9
2.4.6 How many registers are needed to carry out the MIPS assembly as written above? If you could rewrite the code above, what is the minimal number of registers needed?
Solution:
a. 5 as written, 5 minimally
b. 7 as written, 6 minimally

## Slide 10: Exercise 2.6
The following problems deal with translating from C to MIPS. Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively. Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively. Assume that the elements of arrays A and B are 4-byte words:
a. f = -g+h+B[1]
b. f=A[B[g]+1]

## Slide 11
2.6.1 For the C statement above, what is the corresponding MIPS assembly code?
Solution:
a. lw $t0, 4($s7) # $t0 <-- B[1]
sub $t0, $t0, $s1 # $t0 <-- B[1] − g
add $s0, $t0, $s2 # f <-- B[1] −g + h
b. sll $t0, $s1, 2 # $t0 <-- 4*g
add $t0, $t0, $s7 # $t0 <-- Addr(B[g])
lw $t0, 0($t0) # $t0 <-- B[g]
addi $t0, $t0, 1 # $t0 <-- B[g]+1
sll $t0, $t0, 2 # $t0 <-- 4*(B[g]+1) = Addr(A[B[g]+1])
add $t0, $t0, $s6
lw $s0, 0($t0) # f <-- A[B[g]+1]

## Slide 12
2.6.2 For the C statements above, how many MIPS assembly instructions are needed to perform the C statement?
Solution:
a. 3
b. 6

## Slide 13
2.6.3 For the C statements above, how many registers are needed to carry out the C statement using MIPS assembly code?
Solution:
a. 5
b. 4

## Slide 14
The following problems deal with translating from MIPS to C. The following problems deal with translating from C to MIPS. Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively. Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively.
a. sub $s0, $s0, $s1
sub $s0, $s0, $s3
add $s0, $s0, $s1
b. addi $t0, $s6, 4
add $t1, $s6, $0
sw $t1, 0($t0)
lw $t0, 0($t0)
add $s0, $t1, $t0

## Slide 15
The following problems deal with translating from MIPS to C. The following problems deal with translating from C to MIPS. Assume that the variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively. Assume that the base address of the arrays A and B are in registers $s6 and $s7, respectively.
a. sub $s0, $s0, $s1 // f=f-g
sub $s0, $s0, $s3 // f=f-g-i
add $s0, $s0, $s1 //f=f-i
b. addi $t0, $s6, 4 // t0=&(A[1])
add $t1, $s6, $0 // t1=&A[0]
sw $t1, 0($t0) // A[1]= &A[0]
lw $t0, 0($t0) // t0=&A[0]
add $s0, $t1, $t0 // f0=&A[0]+&A[0]

## Slide 16
2.6.4 For the MIPS assembly instructions above, what is the corresponding C statement?
Solution:
a. f = f – i;
b. f = 2 * (&A);

## Slide 17
2.6.5 For the MIPS assembly above, assume that the registers $s0, $s1, $s2, and $s3 contain the values 0x0000000a, 0x00000014, 0x0000001e, and 0x00000028, respectively. Also, assume that register $s6 contains the value 0x00000100, and that memory contains the following values:
Find the value of $s0 at the end of the assembly code.
Solution:
a. $s0 = −30 // add $s0, $s0, $s1 //f=f-i
b. $s0 = 512 //f0=&A[0]+&A[0]
Address | Value
0x00000100 | 0x00000064
0x00000104 | 000000c8
0x00000108 | 0000012c

## Slide 18
2.6.6 For each MIPS instruction, show the value of the opcode(OP), source register(RS), and target register(RT) fields. For the I-type instructions, show the value of the immediate field, and for the R-type instructions, show the value of the desination register(RD) field.
Solution:
a | Type | opcode | rs | rt | rd | immed
sub $s0,$s0, $s1 | R-type | 0 | 16 | 17 | 16 | 
sub $s0, $s0, $s3 | R-type | 0 | 16 | 19 | 16 | 
add $s0, $s0, $s1 | R-type | 0 | 16 | 17 | 16 | 
b | Type | opcode | rs | rt | rd | immed
addi $t0, $s6, 4 | I-type | 8 | 22 | 8 |  | 4
add $t1, $s6, $0 | R-type | 0 | 22 | 0 | 9 | 
sw $t1, 0($t0) | I-type | 43 | 8 | 9 |  | 0
lw $t0, 0($t0) | I-type | 35 | 8 | 8 |  | 0
add $s0, $t1, $t0 | R-type | 0 | 9 | 8 | 16 | 

## Slide 19: Exercise 2.14
The following figure shows the placement of a bit field in register $t0.
In the following problems, you will be asked to write MIPS instructions to extract the bits “Field” from register $t0 and place them into register $t1 at the location indicated in the following table.
Field
31
i, i-1
j,j-1
0
32 - i bits
i – j bits
j bits
0 0 0 … 0 0 0
Field
31
31 – (i - j)
0
1 1 1 … 1 1 1
Field
1 1 1 … 1 1 1
31
14 + i – j bits
14
0
a
b

## Slide 20
2.14.1 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 22 and j = 5 and places the field into $t1 in the format shown in the data table.
Solution:
a. lui $t1, 0x003f //
ori $t1, $t1, 0xffe0
and $t1, $t0, $t1
srl $t1, $t1, 5
b. lui $t1, 0x003f (reverse the pattern)
ori $t1, $t1, 0xffe0
or $t1, $t0, $t1
sll $t1, $t1, 9

## Slide 21
2.14.2 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 4 and j = 0 and places the field into $t1 in the format shown in the data table.
Solution:
a. add $t1, $t0, $0
sll $t1, $t1, 28
b. andi $t0, $t0, 0x000f
sll $t0, $t0, 14
ori $t1, $t1, 0x3fff
sll $t1, $t1, 18
ori $t1, $t1, 0x3fff
or $t1, $t1, $t0

## Slide 22
2.14.3 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 31 and j = 28 and places the field into $t1 in the format shown in the data table.
Solution:
a. srl $t1, $t0, 28
sll $t1, $t1, 29
b. srl $t0, $t0, 28
andi $t0, $t0, 0x0007
sll $t0, $t0, 14
ori $t1, $t1, 0x7fff
sll $t1, $t1, 17
ori $t1, $t1, 0x3fff
or $t1, $t1, $t0

## Slide 23
In the following problems, you will be asked to write MIPS instructions to extract the bits “Field” from register $t0 shown in the figure and place them into register $t1 at the location indicated in the following table. The bits shown as “XXX” are to remain unchanged.
X X X … X X X
Field
31
31 – (i - j)
0
a
X X X … X X X
Field
X X X … X X X
31
14 + i – j bits
14
0
b

## Slide 24
2.14.4 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 17 and j = 11 and places the field into $t1 in the format shown in the data table.
Solution:
a. srl $t0, $t0, 11
sll $t0, $t0, 26
ori $t2, $0, 0x03ff
sll $t2, $t2, 16
ori $t2, $t2, 0xffff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 25
2.14.4 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 17 and j = 11 and places the field into $t1 in the format shown in the data table.
Solution:
b. srl $t0, $t0, 11
sll $t0, $t0, 26
srl $t0, $t0, 12
ori $t2, $0, 0xfff0
sll $t2, $t2, 16
ori $t2, $t2, 0x3fff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 26
2.14.5 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 5 and j = 0 and places the field into $t1 in the format shown in the data table.
Solution:
a. sll $t0, $t0, 27
ori $t2, $0, 0x07ff
sll $t2, $t2, 16
ori $t2, $t2, 0xffff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 27
2.14.5 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 5 and j = 0 and places the field into $t1 in the format shown in the data table.
Solution:
b. sll $t0, $t0, 27
srl $t0, $t0, 13
ori $t2, $0, 0xfff8
sll $t2, $t2, 16
ori $t2, $t2, 0x3fff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 28
2.14.6 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 31 and j = 29 and places the field into $t1 in the format shown in the data table.
Solution:
a. srl $t0, $t0, 29
sll $t0, $t0, 30
ori $t2, $0, 0x3fff
sll $t2, $t2, 16
ori $t2, $t2, 0xffff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 29
2.14.6 Find the shortest sequence of MIPS instructions that extracts a field from $t0 for the constant values i = 31 and j = 29 and places the field into $t1 in the format shown in the data table.
Solution:
b. srl $t0, $t0, 29
sll $t0, $t0, 30
srl $t0, $t0, 16
ori $t2, $0, 0xffff
sll $t2, $t2, 16
ori $t2, $t2, 0x3fff
and $t1, $t1, $t2
or $t1, $t1, $t0

## Slide 30: Exercise 2.20
This exercise deals with recursive procedure calls. For the following problems, the table has an assembly code fragment that computes the factorial of a number. However, the entries in the table have errors, and you will be asked to fix these errors. For number n, factorial of n = 1×2×3×…×n.

## Slide 31
a.FACT: sw $ra, 4($sp)
sw $a0, 0($sp)
addi $sp, $sp, -8
slti $t0, $a0, 1
beq $t0, $0, L1
addi $v0, $0, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal FACT
addi $sp, $sp, 8
lw $a0, 0($sp)
lw $ra, 4($sp)
mul $v0, $a0, $v0
jr $ra
b.FACT: addi $sp, $sp, 8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $s0, $0, $a0
slti $t0, $a0, 2
beq $t0, $0, L1
mul $v0, $s0, $v0
addi $sp, $sp, -8
jr $ra
L1: addi $a0, $a0, -1
jal FACT
addi $v0, $0, 1
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, -8
jr $ra

## Slide 32
2.20.1 The MIPS assembly program above computes the factorial of a given input. The register input is passed through register $a0, and the result is returned in register $v0. In the assembly code, there are a few errors. Correct the MIPS errors.

## Slide 33
Solution:
a.
FACT:
addi $sp, $sp, −8 # make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # $t0 = $a0 x 2
beq, $t0, $0, L1 # if $t0 = 0, goto L1
add $v0, $0, 1 # return 1
add $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1:
addi $a0, $a0, −1 # subtract 1 from argument
jal FACT # call fact(n−1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
add $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n−1)
jr $ra # return to the caller

## Slide 34
Solution:
b.
FACT:
addi $sp, $sp, −8 # make room in stack for 2 more items
sw $ra, 4($sp) # save the return address
sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # $t0 = $a0 x 2
beq, $t0, $0, L1 # if $t0 = 0, goto L1
add $v0, $0, 1 # return 1
add $sp, $sp, 8 # pop two items from the stack
jr $ra # return to the instruction after jal
L1:
addi $a0, $a0, −1 # subtract 1 from argument
jal FACT # call fact(n−1)
lw $a0, 0($sp) # just returned from jal: restore n
lw $ra, 4($sp) # restore the return address
add $sp, $sp, 8 # pop two items from the stack
mul $v0, $a0, $v0 # return n*fact(n−1)
jr $ra # return to the caller

## Slide 35
2.20.2 For the recursive factorial MIPS program above, assume that the input is 4. Rewrite the factorial program to operate in a non-recursive manner. Restrict your register usage to registers $s0-$s7. What is the total number of instructions used to execute your solution from 2.20.2 versus the recursive version of the factorial program?

## Slide 36
Solution:
a.
25 MIPS instructions to execute non-recursive vs. 45 instructions to execute (corrected version of) recursion
Non-recursive version:
FACT: addi $sp, $sp, −4
sw $ra, 4($sp)
add $s0, $0, $a0
add $s2, $0, $1
LOOP: slti $t0, $s0, 2
bne $t0, $0, DONE
mul $s2, $s0, $s2
addi $s0, $s0, −1
j LOOP
DONE: add $v0, $0, $s2
lw $ra, 4($sp)
addi $sp, $sp, 4
jr $ra

## Slide 37
Solution:
b.
25 MIPS instructions to execute non-recursive vs. 45 instructions to execute (corrected version of) recursion
Non-recursive version:
FACT: addi $sp, $sp, −4
sw $ra, 4($sp)
add $s0, $0, $a0
add $s2, $0, $1
LOOP: slti $t0, $s0, 2
bne $t0, $0, DONE
mul $s2, $s0, $s2
addi $s0, $s0, −1
j LOOP
DONE: add $v0, $0, $s2
lw $ra, 4($sp)
addi $sp, $sp, 4
jr $ra

## Slide 38
2.20.3 Show the contents of the stack after each function call, assuming that the input is 4.

## Slide 39
Solution:
a.
Recursive version
FACT: addi $sp, $sp, −8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $s0, $0, $a0
HERE: slti $t0, $a0, 2
beq $t0, $0, L1
addi $v0, $0, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, −1
jal FACT
mul $v0, $s0, $v0
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra

## Slide 40
Solution:
a.
at label HERE, after calling function FACT with input of 4:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
$sp-> −8 contents of register $a0
at label HERE, after calling function FACT with input of 3:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
$sp -> −16 contents of register $a0

## Slide 41
Solution:
a.
at label HERE, after calling function FACT with input of 2:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
−16 contents of register $a0
−20 contents of register $ra
$sp -> −24 contents of register $a0

## Slide 42
Solution:
a.
at label HERE, after calling function FACT with input of 1:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
−16 contents of register $a0
−20 contents of register $ra
−24 contents of register $a0
−28 contents of register $ra
$sp -> −32 contents of register $a0

## Slide 43
Solution:
b.
Recursive version
FACT: addi $sp, $sp, −8
sw $ra, 4($sp)
sw $a0, 0($sp)
add $s0, $0, $a0
HERE: slti $t0, $a0, 2
beq $t0, $0, L1
addi $v0, $0, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, −1
jal FACT
mul $v0, $s0, $v0
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
jr $ra

## Slide 44
Solution:
b.
at label HERE, after calling function FACT with input of 4:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
$sp-> −8 contents of register $a0
at label HERE, after calling function FACT with input of 3:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
$sp -> −16 contents of register $a0

## Slide 45
Solution:
b.
at label HERE, after calling function FACT with input of 2:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
−16 contents of register $a0
−20 contents of register $ra
$sp -> −24 contents of register $a0

## Slide 46
Solution:
b.
at label HERE, after calling function FACT with input of 1:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $a0
−12 contents of register $ra
−16 contents of register $a0
−20 contents of register $ra
−24 contents of register $a0
−28 contents of register $ra
$sp -> −32 contents of register $a0

## Slide 47
For the following problems, the table has an assembly code fragment that computes a Fibonacci number. However, the entries in the table have errors, and you will be asked to fix the errors. For number n, the Fibonacci of n is calculated as follows:
n Fibonacci of n
1 1
2 1
3 2
4 3
5 5
6 8
7 13
8 21

## Slide 48
a.
FIB: addi $sp, $sp, -12
sw $ra, 0($sp)
sw $s1, 4($sp)
sw $a0, 8($sp)
slti $t0, $a0, 1
beq $t0, $0, L1
addi $v0, $a0, $0
j EXIT
L1: addi $a0, $a0, -1
jal FIB
addi $s1, $v0, $0
addi $a0,$a0, -1
jal FIB
add $v0, $v0, $s1
EXIT:lw $ra, 0($sp)
lw $a0, 8($sp)
lw $s1, 4($sp)
addi $sp, $sp, 12
jr $ra
b.
FIB: addi $sp, $sp, -12
sw $ra, 8($sp)
sw $s1, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 3
beq $t0, $0, L1
addi $v0, $0, 1
j EXIT
L1: addi $a0, $a0, -1
jal FIB
addi $a0, $a0, -2
jal FIB
add $v0, $v0, $s1
EXIT:lw $a0, 0($sp)
lw $s1, 4($sp)
lw $ra, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 49
2.20.4 The MIPS assembly program above computes the Fibonacci of a given input. The integer input is passed through register $a0, and the result is returned in register $v0. In the assembly code, there are a few errors. Correct the MIPS errors.

## Slide 50
Solution:
a.
FIB:
addi $sp, $sp, −12
sw $ra, 8($sp)
sw $s1, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 3
beq $t0, $0, L1
addi $v0, $0, 1
j EXIT
L1:
addi $a0, $a0, −1
jal FIB
addi $s1, $v0, $0
addi $a0, $a0, −1
jal FIB
add $v0, $v0, $s1
EXIT:
lw $a0, 0($sp)
lw $s1, 4($sp)
lw $ra, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 51
Solution:
b.
FIB:
addi $sp, $sp, −12
sw $ra, 8($sp)
sw $s1, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 3
beq $t0, $0, L1
addi $v0, $0, 1
j EXIT
L1:
addi $a0, $a0, −1
jal FIB
addi $s1, $v0, $0
addi $a0, $a0, −1
jal FIB
add $v0, $v0, $s1
EXIT:
lw $a0, 0($sp)
lw $s1, 4($sp)
lw $ra, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 52
2.20.5 For the recursive Fibonacci MIPS program above, assume that the input is 4. Rewrite the Fibonacci program to operate in a non-recursive manner. Restrict your register usage to registers $s0 - $s7. What is the total number of instructions used to execute your solution from 2.20.2 versus the recursive version of the factorial program?

## Slide 53
Solution:
a.
23 MIPS instructions to execute non-recursive vs. 73 instructions to execute (corrected version of) recursion.
Non-recursive version:
FIB:
addi $sp, $sp, −4
sw $ra, ($sp)
addi $s1, $0, 1
addi $s2, $0, 1
LOOP:
slti $t0, $a0, 3
bne $t0, $0, EXIT
add $s3, $s1, $0
add $s1, $s1, $s2
add $s2, $s3, $0
addi $a0, $a0, −1
j LOOP
EXIT:
add $v0, s1, $0
lw $ra, ($sp)
addi $sp, $sp, 4
jr $ra

## Slide 54
Solution:
b.
23 MIPS instructions to execute non-recursive vs. 73 instructions to execute (corrected version of) recursion:
Non-recursive version:
FIB:
addi $sp, $sp, −4
sw $ra, ($sp)
addi $s1, $0, 1
addi $s2, $0, 1
LOOP:
slti $t0, $a0, 3
bne $t0, $0, EXIT
add $s3, $s1, $0
add $s1, $s1, $s2
add $s2, $s3, $0
addi $a0, $a0, −1
j LOOP
EXIT:
add $v0, s1, $0
lw $ra, ($sp)
addi $sp, $sp, 4
jr $ra

## Slide 55
2.20.6 Show the content of the stack after each function call, assuming that the input is 4.
Solution:
a.
Recursive version
FIB:
addi $sp, $sp, −12
sw $ra, 8($sp)
sw $s1, 4($sp)
sw $a0, 0($sp)
HERE:
slti $t0, $a0, 3
beq $t0, $0, L1
addi $v0, $0, 1
j EXIT
L1:
addi $a0, $a0, −1
jal FIB
addi $s1, $v0, $0
addi $a0, $a0, −1
jal FIB
add $v0, $v0, $s1
EXIT:
lw $a0, 0($sp)
lw $s1, 4($sp)
lw $ra, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 56
a.
At label HERE, after calling function FIB with input of 4:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $s1
$sp -> −12 contents of register $a0

## Slide 57
Solution:
b.
Recursive version
FIB:
addi $sp, $sp, −12
sw $ra, 8($sp)
sw $s1, 4($sp)
sw $a0, 0($sp)
HERE:
slti $t0, $a0, 3
beq $t0, $0, L1
addi $v0, $0, 1
j EXIT
L1:
addi $a0, $a0, −1
jal FIB
addi $s1, $v0, $0
addi $a0, $a0, −1
jal FIB
add $v0, $v0, $s1
EXIT:
lw $a0, 0($sp)
lw $s1, 4($sp)
lw $ra, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 58
b.
At label HERE, after calling function FIB with input of 4:
old $sp -> 0xnnnnnnnn ???
−4 contents of register $ra
−8 contents of register $s1
$sp -> −12 contents of register $a0