## Slide 1: SOLUTIONS CHAPTER 4

## Slide 2: EXERCISE 4.9
In this exercise we examine the operation of the single-cycle datapath for a particular instruction. Problems in this exercise refer to the following MIPS instruction:
 | Instruction
a | SW R4, -100(R16)
b | SLT R1, R2, R3

## Slide 3
4.9.1 What is the value of the instruction word?
Solution:
 | Binary | Hexadecimal
a | 101011 10000 00100 0000000001100100 | AA040064
b | 000000 00010 00011 00001 00000 101010 | 0043082A

## Slide 4
4.9.2 What is the register number supplied to the register file’s “read register 1” input? Is this register actually read? How about “read register 2”?
Solution:
 | Read Register 1 | Actually Read? | Read Register 2 | Actually Read?
a | 16 (10000b) | Yes | 4 (00100b) | Yes
b | 2 (00010b) | Yes | 3 (00011b) | Yes

## Slide 5
4.9.3 What is the register number supplied to the register file’s “write register” input? Is this register actually written?
Solution:
 | Read Register 1 | Register Actually Written?
a | Either 4 (00100b) or 0 (don’t know because RegDst is X) | No
b | 1 (00001b) | Yes

## Slide 6
Different instructions require different control signals to be asserted in the datapath. The remaining problems in this exercise refer to the following two control signals from Figure 4.24.
 | Control signal 1 | Control signal 2
a | ALUSrc | Branch
b | Jump | RegDst

## Slide 8
4.9.4 What is the value of these two signals for this instruction?
Solution:
 | Control signal 1 | Control signal 2
a | ALUSrc=1 | Branch=0
b | Jump=0 | RegDst=1

## Slide 9
4.9.5 For the datapath from figure 4.24, draw the logic diagram for the part of the control unit that implements just the first signal. Assure that we only need to support LW, SW, BEQ, ADD, and J(jump) instructions.
Solution:
We use I31 through I26 to denote individual bits of instruction[31:26], which is the input to the Control unit:
a | ALUSrc = I31
b | Jump = (NOT I31) AND I27

## Slide 10
4.9.6 Repeat 4.9.5, but now implement both of these signals.
Solution:
If possible, we try to reuse some or all of the logic needed for one signal to help us compute the other signal at a lower cost:
a | ALUSrc = I31 Branch = I28
b | RegDst = NOT I31 Jump = RegDst AND I27

## Slide 11: EXERCISE 4.10
In this exercise we examine how the clock cycle time of the processor affects the design of the control unit, and vice versa. Problems in this exercise assume that the logic blocks used to implement the datapath have the following latencies.
 | I-Mem | Add | MUX | ALU | Regs | D-Mem | Sign-extend | Shift-left-2 | ALU Ctrl
a | 200ps | 70ps | 20ps | 90ps | 90ps | 250ps | 15ps | 10ps | 30ps
b | 750ps | 200ps | 50ps | 250ps | 300ps | 500ps | 100ps | 5ps | 70ps
To solve the problems in this exercise, it helps to first determine the latencies of different paths inside the processor. Assuming zero latency for the Control unit, the critical path is the path to get the data for a load instruction, so we have I-Mem,Mux, Regs, Mux, ALU, D-Mem, and Mux on this path.

## Slide 12: Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 13
4.10.1 To avoid lengthening the critical path of the datapath shown in Figure 4.24, how much time can the control unit take to generate the MemWrite signal?
Solution:
The Control unit can begin generating MemWrite only after I-Mem is read. It must finish generating this signal before the end of the clock cycle. Note that MemWrite is actually a write-enable signal for D-Mem flip-flops, and the actual write is triggered by the edge of the clock signal, so MemWrite need not arrive before that time. So the Control unit must generate the MemWrite in one clock cycle, minus the I-Mem access time:
 | Critical Path | Maximum Time to Generate MemWrite
a | 200ps + 20ps + 90ps + 20ps + 90ps + 250ps + 20ps = 690ps | 690ps − 200ps = 490ps
b | 750ps + 50ps + 300ps + 50ps + 250ps + 500ps + 50ps = 1950ps | 1950ps − 750ps = 1200ps

## Slide 14
4.10.2 Which control signal in Figure 4.24 has the most slack and how much time does the control unit have to generate if it wants to avoid being on the critical path?
Solution:
All control signals start to be generated after I-Mem read is complete. The most slack a signal can have is until the end of the cycle, and MemWrite and RegWrite are both needed only at the end of the cycle, so they have the most slack. The time to generate both signals without increasing the critical path is the one computed in 4.10.1.

## Slide 15: Time Delay for LW: Critical Path
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA
Register File Access Time
Old Value
New Value
busB
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
ExtOp
Old Value
New Value
ALUSrc
Old Value
New Value
MemtoReg
Old Value
New Value
Address
Old Value
New Value
busW
Old Value
New
Delay through Extender & Mux
Register
Write Occurs
Data Memory Access Time
PC+4
PC+4 PC
Notes: This timing diagram shows the worst case timing of our single cycle datapath which occurs at the load instruction.
Clock to Q time after the clock tick, PC will present its new value to the Instruction memory.
After a delay of instruction access time, the instruction bus (Rs, Rt, ...) becomes valid.
Then three things happens in parallel:
(a) First the Control generates the control signals (Delay through Control Logic).
(b) Secondly, the register file access is to put Rs onto busA.
(c) And we have to sign extended the immediate field to get the second operand (busB).
Here I assume register file access takes longer time than doing the sign extension so we have to wait until busA valid before the ALU can start the address calculation (ALU delay).
With the address ready, we access the data memory and after a delay of the Data Memory Access time, busW will be valid.
And by this time, the control unit would have set the RegWr signal to one so at the next clock tick, we will write the new data coming from memory (busW) into the register file.
+3 = 77 min. (Y:57)

## Slide 16
4.10.3 Which control signal in Figure 4.24 is the most critical to generate quickly and how much time does the control unit have to generate it if it wants to avoid being on the critical path?
Solution:
MemWrite and RegWrite are only needed by the end of the cycle. RegDst, Jump, and MemtoReg are needed one Mux latency before the end of the cycle, so they are more critical than MemWrite and RegWrite. Branch is needed two Mux latencies before the end of the cycle, so it is more critical than these. MemRead is needed one D-Mem plus one Mux latency before the end of the cycle, and D-Mem has more latency than a Mux, so MemRead is more critical than Branch.
I-Mem, Mux, Regs, Mux, ALU, D-Mem, and Mux

## Slide 18
Solution:
ALUOp must get to ALU control in time to allow one ALU Ctrl, one ALU, one D-Mem, and one Mux latency before the end of the cycle. This is clearly more critical than MemRead. Finally, ALUSrc must get to the pre-ALU Mux in time, one Mux, one ALU, one D-Mem, and one Mux latency before the end of the cycle. Again, this is more critical than MemRead. Between ALUOp and ALUSrc, ALUOp is more critical than ALUSrc if ALU control has more latency than a Mux. If ALUOp is the most critical, it must be generated one ALU Ctrl latency before the critical-path signals can go through Mux, Regs, and Mux. If the ALUSrc signal is the most critical, it must be generated while the critical path goes through Mux and Regs.
 | The Most Critical Control Signal Is | Time to Generate It without Affecting the Clock Cycle Time
a | ALUOp (30ps > 20ps) | 20ps + 90ps + 20ps − 30ps = 100ps
b | ALUOp (70ps > 50ps) | 50ps + 300ps + 50ps − 70ps = 330ps

## Slide 19
The remaining problems in this exercise assume that the time needed by the control unit to generate individual control signals is as follows:
 | RegDst | Jump | Branch | Mem Read | Memto Reg | ALUOp | Mem Write | ALUSrc | Reg Write
a | 500ps | 500ps | 450ps | 200ps | 450ps | 200ps | 500ps | 100ps | 500ps
b | 1100ps | 1000ps | 1100ps | 800ps | 1200ps | 300ps | 1300ps | 400ps | 1200ps
For the next three problems, it helps to compute for each signal how much time we have to generate it before it starts affecting the critical path. We already did this for RegDst and RegWrite in 4.10.1, and in 4.10.3 we described how to do it for the remaining control signals. We have:
 | RegDst | Jump | Branch | Mem Read | Memto Reg | ALUOp | Mem Write | ALUSrc | Reg Write
a | 470ps | 470ps | 450ps | 220ps | 470ps | 100ps | 490ps | 110ps | 490ps
b | 1150ps | 1150ps | 1100ps | 650ps | 1150ps | 330ps | 1200ps | 350ps | 1200ps

## Slide 20
The difference between the allowed time and the actual time to generate the signal is called “slack.” For this problem, the allowed time will be the maximum time the signal can take without affecting clock cycle time. If slack is positive, the signal arrives before it is actually needed and it does not affect clock cycle time. If the slack is negative, the signal is late and the clock cycle time must be adjusted. We now compute the slack for each signal:
 | RegDst | Jump | Branch | Mem Read | Memto Reg | ALU Op | Mem Write | ALU Src | Reg Write
a | −30ps | −30ps | 0ps | 20ps | 20ps | −100ps | −10ps | 10ps | −10ps
b | 50ps | 150ps | 0ps | −150ps | −50ps | 30ps | −100ps | −50ps | 0ps

## Slide 21
4.10.4 What is the clock cycle time of the processor?
Solution:
The clock cycle time is what we computed in 4.10.1, plus the absolute value of the most negative slack. We have:
 | Control Signal with the Most Negative Slack Is | Clock Cycle Time with Ideal Control Unit (from 4.10.1) | Actual Clock Cycle Time with These Signal Latencies
a | ALUOp (−100ps) | 690ps | 790ps
b | MemRead (−150ps) | 1950ps | 2100ps

## Slide 22
4.10.5 If you can speed up the generation of control signals, but the cost of the entire processor increases by $1 for each 5ps improvement of a single control signal, which control signals would you speed up and by how much to maximize performance? What is the cost (per processor) of this performance improvement ?
Solution:
It only makes sense to pay to speed up signals with negative slack, because improvements to signals with positive slack cost us without improving performance. Furthermore, for each signal with negative slack, we need to speed it up only until we eliminate all its negative slack, so we have:

## Slide 23
Solution:
 | Signals with Negative Slack | Per-Processor Cost to Eliminate All Negative Slack
a | RegWrite (−10ps) RegDst and Jump (−30ps) ALUOp (−100ps) | 170ps at $1/5ps = $34
b | MemtoReg and ALUSrc (−50ps) MemWrite (−100ps) MemRead (−150ps) | 350ps at $1/5ps = $70

## Slide 24
4.10.6 If the processor is already too expensive, instead of paying to speed it up as we did in 4.10.5, we want to minimize its cost without further slowing it down. If you can use slower logic to implement control signals, saving $1 of the processor cost for each 5ps you add to the latency of a single control signal, which control signals would you slow down and by how much to reduce the processor’s cost without slowing it down?

## Slide 25
Solution:
The signal with the most negative slack determines the new clock cycle time. The new clock cycle time increases the slack of all signals until there is no remaining negative slack. To minimize cost, we can then slow down signals that end up having some (positive) slack. Overall, the cost is minimized by slowing signals down by:
 | RegDst | Jump | Branch | Mem Read | Memto Reg | ALUOp | Mem Write | ALUSrc | Reg Write
a | 70ps | 70ps | 100ps | 120ps | 120ps | 0ps | 90ps | 110ps | 90ps
b | 200ps | 300ps | 150ps | 0ps | 100ps | 180ps | 50ps | 100ps | 150ps

## Slide 26: EXERCISE 4.11
In this exercise we examine in detail how an instruction is executed in a single-cycle datapath. Problems in this exercise refer to a clock cycle in which the processor fetches the following instruction word:
 | Instruction word
a | 101011 00011 00010 0000000000010100
b | 000000 00100 00010 00001 00000 101010

## Slide 28
4.11.1 What are the outputs of the sign-extend and the jump “shift left 2” unit (near the top of Figure 4.24) for this instruction word?
Solution:
 | Sign-Extend | Jump’s Shift-Left-2
a | 00000000000000000000000000010100 | 0001100010000000000001010000
b | 00000000000000000000100000101010 | 0010000010000010000010101000

## Slide 29
4.11.2 What are the values of the ALU control unit’s inputs for this instruction?
Solution:
 | ALUOp[1-0] | Instruction[5-0]
a | 00 | 010100
b | 10 | 101010

## Slide 30
4.11.3 What is the new PC address after this instruction is executed? Highlight the path through which this value is determined.
Solution:
 | New PC | Path
a | PC + 4 | PC to Add (PC + 4) to branch Mux to jump Mux to PC
b | PC + 4 | PC to Add (PC + 4) to branch Mux to jump Mux to PC

## Slide 31
The remaining problems in this exercise assume that data memory is all zeros and that the processor’s registers have the following values at the beginning of the cycle in which the above instruction word is fetched:
 | R0 | R1 | R2 | R3 | R4 | R5 | R6 | R8 | R12 | R31
a | 0 | -1 | 2 | -3 | -4 | 10 | 6 | 8 | 2 | -16
b | 0 | 256 | -128 | 19 | -32 | 13 | -6 | -1 | 16 | -2

## Slide 32
4.11.4 For each Mux, show the values of its data output during the execution of this instruction and these register values.
Solution:
 | WrReg Mux | ALU Mux | Mem/ALU Mux | Branch Mux | Jump Mux
a | 2 or 0 (RegDst is X) | 20 | X | PC + 4 | PC + 4
b | 1 | −128 | 0 | PC + 4 | PC + 4

## Slide 33
4.11.5 For the ALU and the two add units, what are their data input values?
Solution:
 | ALU | Add (PC + 4) | Add (Branch)
a | −3 and 20 | PC and 4 | PC + 4 and 20 × 4
b | −32 and −128 | PC and 4 | PC + 4 and 2090 × 4

## Slide 34
4.11.6 What are the values of all inputs for the “Registers” unit?
Solution:
 | Read Register 1 | Read Register 2 | Write Register | Write Data | RegWrite
a | 3 | 2 | X (2 or 0) | X | 0
b | 4 | 2 | 1 | 0 | 1

## Slide 35: EXERCISE 4.12
In this exercise, we examine how pipelining affects the clock cycle time of the processor. Problems in this exercise assume that individual stages of the datapath have the following latencies:
 | IF | Id | EX | MEM | WB
a | 250ps | 350ps | 150ps | 300ps | 200ps
b | 200ps | 170ps | 220ps | 210ps | 150ps

## Slide 36
4.12.1 What is the clock cycle time in a pipelined and non-pipelined processor?
Solution:
 | Pipelined | Single-Cycle
a | 350ps | 1250ps
b | 1100ps | 950ps

## Slide 37
4.12.2 What is the total latency of an LW instruction in a pipelined and non-pipelined processor?
Solution:
 | Pipelined | Single-Cycle
a | 1750ps | 1250ps
b | 1100ps | 950ps

## Slide 38
4.12.3 If we can split one stage of the pipelined datapath into two new stages, each with half the latency of the original stage, which stage would you split and what is the new clock cycle time of the processor?
Solution:
 | Stage to Split | New Clock Cycle Time
a | ID | 300ps
b | EX | 210ps

## Slide 39
The remaining problems in this exercise assume that instructions executed by the processor are broken down as follows:
 | ALU | BEQ | LW | SW
a | 45% | 20% | 20% | 15%
b | 55% | 15% | 15% | 15%

## Slide 40
4.12.4 Assuming there are no stalls or hazards, what is the utilization of the data memory?
Solution:
a.35%
b.30%

## Slide 41
4.12.5 Assuming there are no stalls or hazards, what is the utilization of the write-register port of the “Register” unit?
Solution:
a.65%
b.70%

## Slide 42
4.12.6 Instead of a single-cycle organization, we can use a multi-cycle organization where each instruction takes multiple cycles but one instruction finishes before another is fetched. In this organization, an instruction only goes through stages it actually needs (e.g., ST only takes 4 cycles because it does not need the WB stage). Compare clock cycle times and execution times with single-cycle, multi-cycle, and pipelined organization.

## Slide 43
Solution:
We already computed clock cycle times for pipelined and single-cycle organizations in 4.12.1, and the multi-cycle organization has the same clock cycle time as the pipelined organization. We will compute execution times relative to the pipelined organization. In single-cycle, every instruction takes one (long) clock cycle. In pipelined, a long-running program with no pipeline stalls completes one instruction in every cycle. Finally, a multi-cycle organization completes an LW in 5 cycles, an SW in 4 cycles (no WB), an ALU instruction in 4 cycles (no MEM), and a BEQ in 4 cycles (no WB). So we have the speedup of pipeline:
 | Multi-Cycle Execution Time Is X Times Pipelined Execution Time, where X is | Single-Cycle Execution Time Is X Times Pipelined Execution Time, Where X Is
a | 0.20 × 5 + 0.80 × 4 = 4.20 | 1250ps/350ps = 3.57
b | 0.15 × 5 + 0.85 × 4 = 4.15 | 950ps/220ps = 4.32

## Slide 44: EXERCISE 4.13
In this exercise, we examine how data dependences affect execution in the basic 5-stage pipeline described in Section 4.5. Problems in this exercise refer to the following sequence of instructions:
 | Instruction Sequence
a | SW R16, -100(R6) LW R4, 8(R16) ADD R5, R4, R4
b | OR R1, R2, R3 OR R2, R1, R4 OR R1, R1, R2

## Slide 45
4.13.1 Indicate dependences and their type.
Solution:
 | Instruction Sequence | Dependences
a | I1: SW R16,–100(R6) I2: LW R4,8(R16) I3: ADD R5,R4,R4 | RAW on R4 from I2 to I3
b | I1: OR R1,R2,R3 I2: OR R2,R1,R4 I3: OR R1,R1,R2 | RAW on R1 from I1 to I2 and I3 RAW on R2 from I2 to I3 WAR on R2 from I1 to I2 WAR on R1 from I2 to I3 WAW on R1 from I1 to I3

## Slide 46
4.13.2 Assume there is no forwarding in this pipelined processor. Indicate hazards and add NOP instructions to eliminate them.
Solution:
In the basic five-stage pipeline WAR and WAW dependences do not cause any hazards. Without forwarding, any RAW dependence between an instruction and the next two instructions (if register read happens in the second half of the clock cycle and the register write happens in the first half). The code that eliminates these hazards by inserting NOP instructions is:

## Slide 47
 | Instruction Sequence | 
a | SW R16,–100(R6) LW R4,8(R16) NOP NOP ADD R5,R4,R4 | Delay I3 to avoid RAW hazard on R4 from I2
b | OR R1,R2,R3 NOP NOP OR R2,R1,R4 NOP NOP OR R1,R1,R2 | Delay I2 to avoid RAW hazard on R1 from I1 Delay I3 to avoid RAW hazard on R2 from I2

## Slide 48
4.13.3 Assume there is full forwarding. Indicate hazards and add NOP instructions to eliminate them.
Solution:
With full forwarding, an ALU instruction can forward a value to the EX stage of the next instruction without a hazard. However, a load cannot forward to the EX stage of the next instruction (but can to the instruction after that). The code that eliminates these hazards by inserting NOP instructions is:
 | Instruction Sequence | 
a | SW R16,–100(R6) LW R4,8(R16) NOP ADD R5,R4,R4 | Delay I3 to avoid RAW hazard on R4 from I2 Value for R4 is forwarded from I2 now
b | OR R1,R2,R3 OR R2,R1,R4 OR R1,R1,R2 | No RAW hazard on R1 from I1 (forwarded) No RAW hazard on R2 from I2 (forwarded)

## Slide 49
 | Without Forwarding | With Full Forwarding | With ALU-ALU Forwarding Only
a | 250ps | 300ps | 290ps
b | 180ps | 240ps | 210ps

## Slide 50
4.13.4 What is the total execution time of this instruction sequence without forwarding and with full forwarding? What is the speedup achieved by adding full forwarding to a pipeline that had no forwarding?
Solution:
The total execution time is the clock cycle time times the number of cycles. Without any stalls, a three-instruction sequence executes in 7 cycles (5 to complete the first instruction, then one per instruction). The execution without forwarding must add a stall for every NOP we had in 4.13.2, and execution forwarding must add a stall cycle for every NOP we had in 4.13.3. Overall, we get:
 | No Forwarding | With Forwarding | Speedup Due to Forwarding
a | (7 + 2) × 250ps = 2250ps | (7 + 1) × 300ps = 2400ps | 0.94 (really a slowdown)
b | (7 + 4) × 180ps = 1980ps | 7 × 240ps = 1680ps | 1.18

## Slide 51
4.13.5 Add NOP instructions to this code to eliminate hazards if there is ALU-ALU forwarding only (no forwarding from the MEM to the EX stage). (ALU转发会有2个时钟周期delay)
Solution:
With ALU-ALU-only forwarding, an ALU instruction can forward to the next instruction, but not to the second-next instruction (because that would be forwarding from MEM to EX). A load cannot forward at all, because it determines the data value in MEM stage, when it is too late for ALU-ALU forwarding. We have:
 | Instruction Sequence | 
a | SW R16,–100(R6) LW R4,8(R16) Stall stall ADD R5,R4,R4 | ALU-ALU forwarding of R4 from I2
b | OR R1,R2,R3 OR R2,R1,R4 OR R1,R1,R2 | ALU-ALU forwarding of R1 from I1 ALU-ALU forwarding of R2 from I2

## Slide 52
4.13.6 What is the total execution time of this instruction sequence with only ALU-ALU forwarding? What is the speedup over a no-forwarding pipeline?
Solution:
 | No Forwarding | With ALU-ALU Forwarding Only | Speedup with ALU-ALU Forwarding
a | (7 + 2) × 250ps = 2250ps | 7 × 290ps = 2030ps | 1.11
b | (7 + 4) × 180ps = 1980ps | 7 × 210ps = 1470ps | 1.35

## Slide 53
Exercise 4.16: The first three problems in this exercise refer to the following MIPS instruction
Instruction | 
a | SW R16, -100 (R6)
b | OR R2, R1, R0

## Slide 54
Q: 4.16.1 As this instruction executes, what is kept in each register located between two pipeline stages?
Answer:
  PC – 32 bits
  IF/ID – 64 bits (PC+4, instruction)
  ID/EX – 9 + 32x4 + 10 = 147 (control signals+PC+4 (32), IMM (32), RS(32), RT(32), RT (5), RD(5))
  EX/MEM – 5 + 1 + 32x3 + 5 = 107 (Mem&WB control signals+zero+ALUout+Branch address+rt+(rt or rd’s address))
  MEM/WB – 2 + 32x2 + 5 = 71 (WB address+MEM+ALUout+(rt or rd’s address)))

## Slide 55
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
Notes: How many bits wide is each pipeline register?
PC – 32 bits
IF/ID – 64 bits (PC+4, instruction)
ID/EX – 9 + 32x4 + 10 = 147 (控制信号+PC+4 (32), IMM (32), RS(32), RT(32), RT (5), RD(5))
EX/MEM – 5 + 1 + 32x3 + 5 = 107 (Mem&WB控制信号+zero+ALUout+Branch address+rt+(rt or rd’s address))
MEM/WB – 2 + 32x2 + 5 = 71 (WB地址+MEM+ALUout+(rt or rd’s address)))