## Slide 1: DNS Cache Poisoning Attack Reloaded: Revolutions with Side Channels
Keyu Man, Zhiyun Qian, Zhongjie Wang,
Xiaofeng Zheng†, Youjun Huang†, Haixin Duan†
†
CCS 2020 Best Paper Award

## Slide 2: Contents
Background
  DNS Cache Poisoning
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
Our Attacks
Defenses
Conclusion

## Slide 3: DNS

## Slide 12: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
5.6.7.8
Trudy (Off-path)

## Slide 13: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
? (16 bit)
? (16 bit)
IP Layer | Src: 5.6.7.8 | 
 | Dst: (resolver) | 
UDP Layer | Src Port: 53 | Dst Port:
DNS Layer | TxID: | 
 | Question: www.bank.com A ? | 
 | Answer: www.bank.com A 6.6.6.6, TTL=99999 | 
5.6.7.8
Trudy (Off-path)

## Slide 14: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
? (16 bit)
? (16 bit)
IP Layer | Src: 5.6.7.8 | 
 | Dst: (resolver) | 
UDP Layer | Src Port: 53 | Dst Port:
DNS Layer | TxID: | 
 | Question: www.bank.com A ? | 
 | Answer: www.bank.com A 6.6.6.6, TTL=99999 | 
5.6.7.8
Trudy (Off-path)
Ephemeral Port=Client Port Q:12345->53 | 
Resolver R:53->12345 | NS

## Slide 15: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
? (16 bit)
? (16 bit)
IP Layer | Src: 5.6.7.8 | 
 | Dst: (resolver) | 
UDP Layer | Src Port: 53 | Dst Port:
DNS Layer | TxID: | 
 | Question: www.bank.com A ? | 
 | Answer: www.bank.com A 6.6.6.6, TTL=99999 | 
5.6.7.8
Trudy (Off-path)
Ephemeral Port=Client Port Q:12345->53 | 
Resolver R:53->12345 | NS

## Slide 16: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
Traditional: 216 × 216 = 232 (Impossible in short time)
Our Side Channel: 216 + 216 ≈ 216
? (16 bit)
? (16 bit)
IP Layer | Src: 5.6.7.8 | 
 | Dst: (resolver) | 
UDP Layer | Src Port: 53 | Dst Port:
DNS Layer | TxID: | 
 | Question: www.bank.com A ? | 
 | Answer: www.bank.com A 6.6.6.6, TTL=99999 | 
5.6.7.8
Trudy (Off-path)
Ephemeral Port=Client Port Q:12345->53 | 
Resolver R:53->12345 | NS

## Slide 17: DNS Cache Poisoning
www.bank.com IP=6.6.6.6
Resolver
Traditional: 216 × 216 = 232 (Impossible in short time)
Our Side Channel: 216 + 216 ≈ 216
? (16 bit)
? (16 bit)
IP Layer | Src: 5.6.7.8 | 
 | Dst: (resolver) | 
UDP Layer | Src Port: 53 | Dst Port:
DNS Layer | TxID: | 
 | Question: www.bank.com A ? | 
 | Answer: www.bank.com A 6.6.6.6, TTL=99999 | 
5.6.7.8
Trudy (Off-path)
Ephemeral Port=Client Port Q:12345->53 | 
Resolver R:53->12345 | NS

## Slide 18: Attack workflow

## Slide 19: Contents
Background
Part I: Infer Ephemeral Port
  Side-channel-based Scan
Part II: Extend Attack Window
Our Attacks
Defenses
Conclusion

## Slide 20: Port Inference: Basics
Resolver
Attacker
UDP dport=53
UDP dport=67
ICMP: 67 isn’t open
OS
APP
Packet
Listen on 53

## Slide 21: Port Inference: Ephemeral Ports
Resolver
Attacker
UDP dport=1234
Nameserver
UDP dport=1234
ICMP: 1234 isn’t open
DNS Query
(Ephemeral Port) 1234->53

## Slide 22: Port Inference: IP Spoofing
Resolver
5.6.7.8
Attacker
5.6.7.8
Nameserver
UDP dport=1234
ICMP: 5678 isn’t open
UDP dport=5678

## Slide 23: Port Inference:
Side Channel

## Slide 24: Port Inference:
Side Channel
9
Off-Path TCP Exploits: Global Rate Limit Considered Dangerous
USENIX Security 2016
ICMP Global Rate Limit:
  Limit sending rate
  Shared by all IPs
50 ICMPs / 50 ms

## Slide 25: Port Inference:
Side Channel
9
Off-Path TCP Exploits: Global Rate Limit Considered Dangerous
USENIX Security 2016
ICMP Global Rate Limit:
  Limit sending rate
  Shared by all IPs
50 ICMPs / 50 ms

## Slide 26: Port Inference: How It Works
Resolver
with ONE port open
Spoofed
50 UDP Probes
50 ICMPs
Verification
49 ICMPs
Verification
ICMP Reply
Attacker
Nameserver
Resolver
with NO port open
Nameserver
Counter=50
Counter=50-50=0
Counter=50
Counter=50-49=1
Normal
50 UDP Probes
Attacker
Hit 50 closed ports
Hit 49 closed ports &
1 open port

## Slide 27: Port Inference: Measurement

## Slide 28: Port Inference: Measurement
Open Resolvers:
  34% Vulnerable
Well-known Public Resolvers:
  12/14 Vulnerable

## Slide 29: Contents
Background
Overview
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
  Strategy I: Malicious Name Server (Refer to the Paper)
  Strategy II: Response Rate Limiting
Our Attacks
Defenses
Conclusion

## Slide 30: Extend Attack Window
Query
ry
Resp
onse
Que
Fake
Response
Flooding
Queries
Attack
Window

## Slide 31: Extend Attack Window
Query
ry
Que
Flooding
Queries
nse
Attack
Window
RRL: 18%
Deployed
Respo

## Slide 32: Extend Attack Window

## Slide 33: Contents
Background
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
Our Attacks
  Forwarder Attack
  Resolver Attack
Defenses
Conclusion

## Slide 34
Forwarder Attack: Results
Device: Xiaomi R3 Wi-Fi Router
Upstream DNS server: 1.1.1.1
Success rate: 20/20
Average time-to-succeed: 271s

## Slide 35: Contents
Background
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
Our Attacks
  Forwarder Attack (Refer to the Paper)
  Resolver Attack
Defenses
Conclusion

## Slide 38: Resolver Attack: Results

## Slide 39: Contents
Background
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
Our Attacks
Defenses
Conclusion

## Slide 40: Defenses
DNSSEC
0x20 encoding
DNS cookie
  Only 5% open resolvers deployed
Disable ICMP port unreachable
Randomize ICMP global rate limit

## Slide 41: Contents
Background
Part I: Infer Ephemeral Port
Part II: Extend Attack Window
Our Attacks
Defenses
Conclusion

## Slide 42: Conclusion
Side-channel-based UDP port scan.
Make DNS cache poisoning possible again!
Real-world attacks.