## Slide 1
Networking Overview: “Everything” you need to know, in 50 minutes
Network Security
Prof. Haojin Zhu
Adopted from David Wagner @ UC Berkeley
May 8, 2019

## Slide 2: Local-Area Networks
point-to-point
shared
How does computer A send a message to computer C?
A
C

## Slide 3: Local-Area Networks: Packets
From: A To: C
Message: Hello world!
A | C
Hello world! | 
A | C | Hello world!

## Slide 4: Wide-Area Networks
How do we connect two LANs?
router C
A

## Slide 5: Wide-Area Networks
5
How do we connect two LANs?
router C
C.com
A.com
Hello
world!
A
R
A
R
C
C.com
A.com
Hello world!
A.com | C.com
Hello world! | 

## Slide 6: Key Concept #1: Protocols
6
A protocol is an agreement on how to communicate
Includes syntax and semantics
  How a communication is specified & structured
o Format, order messages are sent and received
  What a communication means
o Actions taken when transmitting, receiving, or timer expires
Example: making a comment in lecture?
Raise your hand.
Wait to be called on.
Or: wait for speaker to pause and vocalize
4. If unrecognized (after timeout): say “excuse me”

## Slide 7: Key Concept #2: Dumb Network
7
Original Internet design: interior nodes (“routers”) have no knowledge* of ongoing connections going through them
Not how you picture the telephone system works
  Which internally tracks all of the active voice calls
Instead: the postal system!
  Each Internet message (“packet”) self-contained
* Today’s Internet is full of hacks that violate this

## Slide 8
Self-Contained IP Packet Format
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit Flags
13-bit Fragment Offset
8-bit Time to Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload (remainder of message)
.
.
.
.
.
Header is like a letter envelope: contains all info needed for delivery
IP = Internet Protocol

## Slide 9: Key Concept #2: Dumb Network
9
Original Internet design: interior nodes (“routers”) have no knowledge* of ongoing connections going through them
Not: how you picture the telephone system works
  Which internally tracks all of the active voice calls
Instead: the postal system!
  Each Internet message (“packet”) self-contained
  Interior routers look at destination address to forward
  If you want smarts, build it “end-to-end”, not “hop-by-hop”
  Buys simplicity & robustness at the cost of shifting complexity into end systems
* Today’s Internet is full of hacks that violate this

## Slide 10: Key Concept #3: Layering
Internet design is strongly partitioned into layers
  Each layer relies on services provided by next layer below …
  … and provides services to layer above it
Analogy:
– Consider structure of an application you’ve written and the “services” each layer relies on / provides
System Calls
Device Drivers
Voltage Levels / Magnetic Domains
}
Fully
isolated
from user
programs
Code You Write
Run-Time Library

## Slide 11: Internet Layering (“Protocol Stack”)
7
4
3
2
1
Note on a point of potential confusion: these diagrams are always drawn with lower layers below higher layers …
But diagrams showing the layouts of packets are often the opposite, with the lower layers at the top since their headers precede those for higher layers
Application
Transport
(Inter)Network
Link
Physical

## Slide 12: Horizontal View of a Single Packet
Link Layer Header
(Inter)Network Layer Header (IP)
Transport Layer Header
Application Data: structure depends on the application
…
First bit transmitted

## Slide 13: Vertical View of a Single Packet
13
Link Layer Header
First bit transmitted
(Inter)Network Layer Header (IP)
Transport Layer Header
Application Data: structure depends on the application
.
.
.
.
.
.
.

## Slide 14: Internet Layering (“Protocol Stack”)
7
4
3
2
1
Application
Transport
(Inter)Network
Link
Physical

## Slide 15: Layer 1: Physical Layer
7
4
3
2
1
Encoding bits to send them over a single physical link
e.g. patterns of voltage levels / photon intensities / RF modulation
Application
Transport
(Inter)Network
Link
Physical

## Slide 16: Layer 2: Link Layer
7
4
3
2
1
Framing and transmission of a collection of bits into individual messages sent across a single “subnetwork” (one physical technology)
Might involve multiple physical links (e.g., modern Ethernet)
Often technology supports broadcast transmission (every “node” connected to subnet receives)
Application
Transport
(Inter)Network
Link
Physical

## Slide 17: Layer 3: (Inter)Network Layer (IP)
7
4
3
2
1
Bridges multiple “subnets” to provide end-to-end internet connectivity between nodes
Provides global addressing
Works across different link technologies
}
Different for each
Internet “hop”
Application
Transport
(Inter)Network
Link
Physical

## Slide 18: Layer 4: Transport Layer
7
4
3
2
1
End-to-end communication between processes
Different services provided: TCP = reliable byte stream UDP = unreliable datagrams
(Datagram = single packet message)
Application
Transport
(Inter)Network
Link
Physical

## Slide 19: Layer 7: Application Layer
7
4
3
2
1
Communication of whatever you wish
Can use whatever transport(s) is convenient
Freely structured E.g.:
Skype, SMTP (email),
HTTP (Web), Halo, BitTorrent
Application
Transport
(Inter)Network
Link
Physical

## Slide 20: Internet Layering (“Protocol Stack”)
7
4
3
2
1
}
Implemented only at hosts,
not at interior router
(“dumb network”)
Application
Transport
(Inter)Network
Link
Physical

## Slide 21: Internet Layering (“Protocol Stack”)
7
4
3
2
1
}
Implemented everywhere
Application
Transport
(Inter)Network
Link
Physical

## Slide 22
Internet Layering (“Protocol Stack”)
7
4
3
2
1
}”
Different for each
Internet “hop
} ~Same for each Internet “hop”
Application
Transport
(Inter)Network
Link
Physical

## Slide 23: Hop-By-Hop vs. End-to-End Layers
Host B
Router 4
Host E
Router 3
Router 5
Router 6
Router 7
Host A communicates with Host D
Host C
Host A
Router 1
Host D
Router 2

## Slide 24: Hop-By-Hop vs. End-to-End Layers
Host A communicates with Host D
Host C
Host A
Router 1
E.g., Wi-Fi
Different Physical & Link Layers (Layers 1 & 2)
Host B
Router 4
Host E
Host D
E.g., Ethernet
Router 3
Router 2
Router 5
Router 6
Router 7

## Slide 25: Hop-By-Hop vs. End-to-End Layers
Host B
Router 4
Host E
Host D
Router 2
Router 3
Router 5
Router 6
Router 7
Host A communicates with Host D
Host C
Host A
Router 1
E.g., HTTP over TCP over IP
Same Network / Transport / Application Layers (3/4/7) (Routers ignore Transport & Application layers)

## Slide 26: Layer 3: (Inter)Network Layer (IP)
26
7
4
3
2
1
Bridges multiple “subnets” to provide end-to-end internet connectivity between nodes
Provides global addressing
Works across different link technologies
Application
Transport
(Inter)Network
Link
Physical

## Slide 27: IP Packet Structure
4-bit 4-bit 8-bit Version Header Type of Service 16-bit Total Length (Bytes) Length (TOS) 3-bit 16-bit Identification Flags 13-bit Fragment Offset 8-bit Time to Live (TTL) 8-bit Protocol 16-bit Header Checksum 32-bit Source IP Address 32-bit Destination IP Address
Options (if any)
Payload

## Slide 28: IP Packet Structure
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Fla
gs
16-bit Header Checksum
13-bit Fragment Offset
8-bit Time to Live (TTL)
8-bit Protocol
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Specifies the length of the entire IP packet: bytes in this header plus bytes in the Payload
Payload

## Slide 29: IP Packet Structure
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Fla
gs 13-bit Fragment Offset
16-bit Header Checksum
8-bit Time to Live (TTL)
8-bit Protocol
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Specifies how to interpret the start of the Payload, which is the header of a Transport Protocol such as TCP or UDP
Payload

## Slide 30: IP Packet Structure
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit Flags
13-bit Fragment Offset
8-bit Time to Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 31: IP Packet Header (Continued)
31
Two IP addresses
–Source IP address (32 bits)
–Destination IP address (32 bits)
Destination address
–Unique identifier/locator for the receiving host
–Allows each node to make forwarding decisions
Source address
–Unique identifier/locator for the sending host
–Recipient can decide whether to accept packet
–Enables recipient to send a reply back to source

## Slide 32: Postal Envelopes:
(Post office doesn’t look at the letter
inside the envelope)
32

## Slide 33: Analogy of IP to Postal Envelopes:
(Routers don’t look at the payload beyond
IP source address
IP destination address
the IP header)

## Slide 34: IP:“Best Effort ” Packet Delivery
Routers inspect destination address, locate “next hop” in forwarding table
  Address = ~unique identifier/locator for the receiving host
Only provides a “I’ll give it a try” delivery service:
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
source
destination
IP network

## Slide 35
“Best Effort ” is Lame! What to do?
It’s the job of our Transport (layer 4) protocols to build services our apps need out of IP’s modest layer-3 service

## Slide 36: Layer 4: Transport Layer
7
4
3
2
1
End-to-end communication between processes
Different services provided: TCP = reliable byte stream UDP = unreliable datagrams
(Datagram = single packet message)
Application
Transport
(Inter)Network
Link
Physical

## Slide 37
“Best Effort” is Lame! What to do?
It’s the job of our Transport (layer 4) protocols to build services our apps need out of IP’s modest layer-3 service
#1 workhorse: TCP (Transmission Control Protocol)
Service provided by TCP:
  Connection oriented (explicit set-up / tear-down)
o End hosts (processes) can have multiple concurrent long-lived communication
  Reliable, in-order, byte-stream delivery
o Robust detection & retransmission of lost data

## Slide 38: TCP “Bytestream” Service
Byte 3
Byte 2
Byte 1
Byte 0
Process A on host H1
Byte 80
Byte 80
Hosts don’t ever see packet boundaries, lost or corrupted packets, retransmissions, etc.
Process B on host H2
Byte 0 | Byte 1 | Byte 2 | Byte 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 39: Bidirectional communication:
Byte 3
Byte 2
Byte 1
Byte 0
Process B on host H2
Byte 73
Byte 73
There are two separate bytestreams, one in each direction
Process A on host H1
Byte 0 | Byte 1 | Byte 2 | Byte 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 40: TCP Header
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 41: TCP Header
Ports are associated with OS processes
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 42
TCP Header
Ports are associated with OS processes
IP source & destination addresses plus TCP source and destination ports uniquely identifies a TCP connection
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
(IP Header)
(Link Layer Header)

## Slide 43: TCP Header
Ports are associated with OS processes
IP source & destination addresses plus TCP source and destination ports uniquely identifies a TCP connection
Some port numbers are
“well known” / reserved
e.g. port 80 = HTTP
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 44: TCP Header
Starting sequence number (byte offset) of data carried in this packet
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 45: TCP Header
Starting sequence number (byte offset) of data carried in this packet
Byte streams numbered independently in each direction
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 46: TCP Header
46
Starting sequence number (byte offset) of data carried in this packet
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Byte stream numbered independently in each direction
Sequence number assigned to start of byte stream is picked when
connection begins; doesn’t start at 0

## Slide 47: TCP Header
Acknowledgment gives seq # just beyond highest seq. received in order.
If sender sends N bytestream bytes starting at seq S then “ack” for it will be S+N.
Source port |  |  | Destination port | 
Sequence number |  |  |  | 
Acknowledgment |  |  |  | 
HdrLen | 0 | Flags |  | Advertised window
Checksum |  |  |  | Urgent pointer
Options (variable) |  |  |  | 
Data |  |  |  | 

## Slide 48: Sequence Numbers
Host B
TCP Data
Host A
ISN (initial sequence number)
TCP Data
TCP HDR
TCP HDR
Sequence
number from A
= 1st byte of data
ACK sequence
number from B
= next expected byte

## Slide 49: TCP Header
Uses include:
acknowledging data (“ACK”)
setting up (“SYN”) and closing connections (“FIN” and
“RST”)
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 50: Establishing a TCP Connection
50
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN+ACK)
  Host A sends an ACK to acknowledge the SYN+ACK
SYN
SYN+A
ACK
A
B
Data
Data
Each host tells its Initial Sequence Number (ISN) to the other host.
(Spec says to pick based on local clock)

## Slide 51: Timing Diagram: 3-Way Handshaking
Client (initiator)
connect()
Server
listen()
SYN, SeqNum = x
SYN + ACK, SeqNum = y, A
k = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
accept()
Different starting initial sequence numbers (ISNs) in each direction

## Slide 52
Extra Material

## Slide 53: Layer 7: Application Layer
7
4
3
2
1
Communication of whatever you wish
Can use whatever transport(s) is convenient
Freely structured E.g.:
Skype, SMTP (email),
HTTP (Web), Halo, BitTorrent
Application
Transport
(Inter)Network
Link
Physical

## Slide 54
GET /index.html HTTP/1.1
Accept: image/gif, image/x-bitmap, image/jpeg, */*
Accept-Language: en Connection: Keep-Alive
User-Agent: Mozilla/1.22 (compatible; MSIE Host: www.example.com
Referer: http://www.google.com?q=dingbats
2.0;
Windows 95)
Web (HTTP) Request
Method
Resource
HTTP version
Headers
Blank line Data (if POST; none for GET)
download data. POST:
GET:
upload data.

## Slide 55
HTTP/1.0 200 OK
Date: Sun, 19 Apr 2009 02:20:42 GMT
Server: Microsoft-Internet-Information-Server/5.0 Connection: keep-alive
Content-Type: text/html
Last-Modified: Sat, 18 Apr 2009 17:39:05 GMT
Set-Cookie: session=44eb; path=/servlets Content-Length: 2543
<HTML> Some data... blah, blah, blah </HTML>
Web (HTTP) Response
HTTP version
Status code
Reason phrase
Headers
Data

## Slide 56: Host Names vs. IP addresses
Host names
–Examples: www.cnn.com and bbc.co.uk
–Mnemonic name appreciated by humans
–Variable length, full alphabet of characters
–Provide little (if any) information about location
IP addresses
–Examples: 64.236.16.20 and 212.58.224.131
–Numerical address appreciated by routers
–Fixed length, binary number
–Hierarchical, related to host location
56

## Slide 57: IP Packet Structure
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit Flags
13-bit Fragment Offset
8-bit Time to Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any) Payload

## Slide 58: IP Packet Header Fields (Continued)
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
End host reassembles to recover original packet
Fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
  Supports dividing a large IP packet into fragments
  … in case a link cannot handle a large IP packet

## Slide 59: Example: E-Mail Message Using MIME
From: jrex@cs.princeton.edu To: feamster@cc.gatech.edu Subject: picture of my cat MIME-Version: 1.0
Content-Transfer-Encoding: base64
Content-Type: image/jpeg
Base64 encoded data ….
JVBERi0xLjMNJeLjz9MNMSAwI
.........................
......base64 encoded data
type and subtype
method used to encode data
MIME version
encoded data

## Slide 60: Example With Received Header
60
Content-Transfer-Encoding: 7bit
Return-Path: <casado@cs.stanford.edu>
Received: from ribavirin.CS.Princeton.EDU (ribavirin.CS.Princeton.EDU [128.112.136.44])
by newark.CS.Princeton.EDU (8.12.11/8.12.11) with SMTP id k04M5R7Y023164 for <jrex@newark.CS.Princeton.EDU>; Wed, 4 Jan 2006 17:05:37 -0500 (EST)
Received: from bluebox.CS.Princeton.EDU ([128.112.136.38])
by ribavirin.CS.Princeton.EDU (SMSSMTP 4.1.0.19) with SMTP id M2006010417053607946 for <jrex@newark.CS.Princeton.EDU>; Wed, 04 Jan 2006 17:05:36 -0500
Received: from smtp-roam.Stanford.EDU (smtp-roam.Stanford.EDU [171.64.10.152]) by bluebox.CS.Princeton.EDU (8.12.11/8.12.11) with ESMTP id k04M5XNQ005204 for <jrex@cs.princeton.edu>; Wed, 4 Jan 2006 17:05:35 -0500 (EST)
Received: from [192.168.1.101] (adsl-69-107-78-147.dsl.pltn13.pacbell.net [69.107.78.147]) (authenticated bits=0)
by smtp-roam.Stanford.EDU (8.12.11/8.12.11) with ESMTP id k04M5W92018875 (version=TLSv1/SSLv3 cipher=DHE-RSA-AES256-SHA bits=256 verify=NOT); Wed, 4 Jan 2006 14:05:32 -0800
Message-ID: <43BC46AF.3030306@cs.stanford.edu> Date: Wed, 04 Jan 2006 14:05:35 -0800
From: Martin Casado <casado@cs.stanford.edu>
User-Agent: Mozilla Thunderbird 1.0 (Windows/20041206) MIME-Version: 1.0
To: jrex@CS.Princeton.EDU
CC: Martin Casado <casado@cs.stanford.edu> Subject: Using VNS in Class
Content-Type: text/plain; charset=ISO-8859-1; format=flowed

## Slide 61: IP Packet Structure
4-bit Version
4-bit Header Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit Flags
13-bit Fragment Offset
8-bit Time to Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any) Payload

## Slide 62: IP Packet Header Fields
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
62

## Slide 63: Sample Email (SMTP) interaction
63
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S:
C:
S:
C:
S:
C:
C:
C:
C:
C:
C:
S:
C:
S:
250 alice@crepes.fr... Sender ok
RCPT TO: <bob@hamburger.edu>
250 bob@hamburger.edu ... Recipient ok
DATA
354 Enter mail, end with "." on a line by
From: alice@crepes.fr
itself
Subject: Do you like ketchup?
How about pickles?
.
250 Message accepted
for delivery
To: hamburger-list@burger-king.com Email header
QUIT Lone period marks end of message
221 hamburger.edu closing connection
Email body

## Slide 64: Future Internet Architecture (FIA) Awards - 2010
Follow on to FIND – Future Internet Design, 50 awards over 5 years
Inform the development of future trustworthy, robust networks
$8M/3 year grant for each of these projects:
Mobility First
NEBULA
eXpressive Internet Architecture (XIA)
Named Data Networking (NDN)

## Slide 65: Mobility First
Members
Rutgers:
D. Raychaudhuri*+
Wade Trappe
UMass - Amherst
Arun Venkataramani#+
Jim Kurose
Umichigan:Z. Morley Mao+
Duke University: Xaiowei Yang+
MIT: Bill Lehr+
U Wisconsin
U Nebraska

## Slide 66: eXpressive Internet Architecture (XIA)
Aditya Akella - CS&S, UW-Madison
David Andersen - CS, CMU
Dan Barrett - CS, CMU (Senior Research Programmer)
John Byers - CS, BU
Laura Dabbish - HCII/Heinz, CMU
David Eckhardt - CS, CMU
Nitin Gupta - CS, CMU
Ruogu Kang - HCI, CMU
Sara Kiesler - HCII, CMU
Yanlin Li - CMU (Research Scientist)
Bruce Maggs - CS, Duke
Duyen Mary Nguyen, HCI, CMU (Post Doc)
Jon Peha - EPP/ECE, CMU
Adrian Perrig - EPP/ECE/CS, CMU
Raja Sambasivan - CS, CMU (Post Doc)
Marvin Sirbu - EPP/ECE, CMU
Chuck Song (Senior Scientist)
Srinivasan Seshan - CS, CMU
Peter Steenkiste (PI) - CS/ECE, CMU
Hui Zhang - CS, CMU

## Slide 67: Named Data Networking (NDN)
Lixia Zhang, Deborah Estrin, and Jeffrey Burke
University of California, Los Angeles
Van Jacobson, James D. Thornton, and Diana K. Smetters
Palo Alto Research Center (PARC)
Beichuan Zhang
University of Arizona
Gene Tsudik
University of California, Irvine
kc claffy and Dmitri Krioukov
University of California, San Diego
Dan Massey and Christos Papadopoulos
Colorado State University
Tarek Abdelzaher
University of Illinois at Urbana-Champaign
Lan Wang
University of Memphis
Patrick Crowley
Washington University
Edmund Yeh
Yale University

## Slide 68: The problem
ISP
ISP
Notes: Current Internet architecture is communication- and comm. end-point-centric. But, the nature of the Internet shifted more towards content. Today’s Internet is radio-hostile; mobile-hostile; causes traffic concentration and congestion. It doesn’t deal well with distribution

## Slide 69: Communication v. Distribution
 | Communication | Distribution
Naming | Endpoints | Content
Security | Secure Process | Secure Content

## Slide 70: Today
src
dst
Path determined by global routing, not local choice
Structural asymmetry precludes market mechanisms and encourages monopoly formation
X
Notes: Today’s internet routing has issues with being a distribution system. There are only a few mechanisms needing change to transform the current Internet from the worst to the best distribution system.

## Slide 71: NDN approach
Producer
Consumer
a/b
Packets say ‘what’ not ‘where’‘(no src or dst)
Forwarding decision is local
Upstream performance is measurable
? a/b/c/e

## Slide 72: We envision replacing this:
ISP
ISP

## Slide 73: With THIS:
ISP
ISP
Notes: Mobility is an issue with endpoint addresses, because they keep changing. In NDN, "Mobility is simply irrelevant” -- nothing associated with the communication changes with mobility.
Rather than naming the moving object (receiver) as in IP, we name the content desired by that object. Clearly things get delivered where you were – not where you are. If you move and simply request them again, you get them from a cache only one or two hops away, assuming incremental mobility.

## Slide 74: Future Internet Architecture Next Phase (FIA-NP) Awards - 2014
Built upon success of FIA. Move from design to piloted deployments in real world setting.
No one architecture will replace Internet wholesale.
$15M total to 3 projects:
  XIA-NP
    Tests in vehicle network and large scale video delivery
  NDN-NP – established industry consortium
    Open mHealth and UCLA Facilities Management
  Mobility First-NP
    Wireless provider, content delivery network, weather emergency notification system

## Slide 75: Group Discussions
Pls discuss the potential attacks towards different layers (physical/link layers, IP layers, transportation layers).